## Slide 1: IoT Sensor & Data Analysis
A proposed temperature and humidity monitoring system
College project presentation
ENVIRONMENTAL MONITORING
Notes: Proposed college project. Hardware, software and collection plan are assumptions to adapt to the actual implementation. Any example results are synthetic and do not represent measured project performance.

## Slide 2: Problem statement and objectives
Problem statement
Manual readings leave gaps between observations and make environmental changes difficult to track.
Project scope
Monitor a room using temperature and humidity readings from one sensor node.
Project objectives
Record readings with timestamps.
Store measurements for later analysis.
Clean missing or invalid readings.
Visualize trends and flag threshold crossings.
Notes: Proposed college project. Hardware, software and collection plan are assumptions to adapt to the actual implementation. Any example results are synthetic and do not represent measured project performance.

## Slide 3: Sensors and system architecture
Sensing
Proposed sensor: DHT22.
Measure temperature (°C) and relative humidity (% RH).
ESP32 reads the sensor at a planned interval of 60 seconds.
Analysis and display
Python and pandas process stored readings.
Matplotlib plots trends.
A dashboard shows recent readings and threshold alerts.
Transmission and storage
ESP32 sends timestamped readings over Wi-Fi.
An MQTT broker passes messages to a collector.
The collector stores records in CSV or a database.
Notes: Proposed college project. Hardware, software and collection plan are assumptions to adapt to the actual implementation. Any example results are synthetic and do not represent measured project performance.

## Slide 4: Dataset and preprocessing
Dataset design
Fields: timestamp, device_id, temperature_c, humidity_pct and quality_flag.
Planned collection: 1 reading per minute for 24 hours.
Expected records: 1,440 for one node, before data loss.
Preprocessing workflow
Parse timestamps and sort records.
Remove duplicate device–timestamp pairs.
Flag missing values and impossible humidity values outside 0–100%.
Mark short interpolated gaps and retain longer gaps as missing.
Notes: Proposed college project. Hardware, software and collection plan are assumptions to adapt to the actual implementation. Any example results are synthetic and do not represent measured project performance.

## Slide 5: Analysis methods
Descriptive statistics
Calculate count, mean, minimum and maximum for each variable.
Report missing-data percentage.
Compare hourly summaries to identify changes over time.
Anomaly detection
Compare readings with configurable thresholds.
Example rule: temperature above 30°C.
Review sudden changes against nearby readings before treating them as real events.
Trend analysis
Plot temperature and humidity separately with units.
Use a five-reading moving average to reduce short-term noise.
Inspect correlation without claiming causation.
Notes: Proposed college project. Hardware, software and collection plan are assumptions to adapt to the actual implementation. Any example results are synthetic and do not represent measured project performance.

## Slide 6: Results and visualizations
28°C
Mean temperature
in the example
1 / 6
Example readings
above 31°C
Illustrative data only, not measured results.
Temperature peaks at 32°C at 12:00.
One of six readings exceeds the 31°C example threshold.
Chart: Temperature (°C)
| 09:00 | 10:00 | 11:00 | 12:00 | 13:00 | 14:00
Temperature (°C) | 24 | 25 | 27 | 32 | 31 | 29
Threshold (°C) | 31 | 31 | 31 | 31 | 31 | 31
Notes: Proposed college project. Hardware, software and collection plan are assumptions to adapt to the actual implementation. Any example results are synthetic and do not represent measured project performance.

## Slide 7: Conclusion and future work
Project conclusion
The proposed workflow connects sensing, storage and analysis in one repeatable process.
The illustrative chart demonstrates how trends and threshold events could appear.
Measured performance still requires a physical prototype and real readings.
Future work
Collect and validate a full day of sensor data.
Compare readings with a reference instrument.
Add more nodes and test network interruptions.
Evaluate alert accuracy and power consumption.
Notes: Proposed college project. Hardware, software and collection plan are assumptions to adapt to the actual implementation. Any example results are synthetic and do not represent measured project performance.